## Slide 1: Knife Safety & Handling — Prep Station
Claw grip, damp towel under boards, never catch a falling knife.

## Slide 2: Owner & Purpose
Document owner: Samuel Okafor (Sous Chef, Prep).
Purpose: prevent cuts, slips, and cross-contamination at the Prep station.
Applies to all knives, mandolines, oyster knives, and cutting boards used in Prep.
Read, follow, and ask Samuel if anything is unclear.

## Slide 3: Core Rules (Do Not Deviate)
Claw grip — fingertips tucked, knuckles guide the blade.
Put a damp towel under every cutting board so it can't slide.
Never catch a falling knife. Step back and let it drop.
Carry knives point down, blade facing back, and call "Sharp, behind!".
Never leave knives in the sink or under water. Wash, dry and return to the magnetic strip.
Cut-resistant glove on the guiding hand for mandolines and oysters.
A dull knife is dangerous: hone before every shift; sharpening service every two weeks.

## Slide 4: Station Setup & Board Control
Set board on a clean, folded damp towel so it can't slide.
Choose the right board size; keep a trash cambro and garnish pan within reach.
Keep blade path clear: no towels, cords, or pans crossing the board.
Wipe and swap boards if the surface grooves or becomes greasy.

## Slide 5: Safe Carry & Traffic Calls
Move with knives at your side: point down, blade facing back.
Call “Sharp, behind!” before stepping into traffic or passing a teammate.
Never carry more than one bare blade per hand; use a rack or tray for multiples.
Place knives down before opening doors, moving carts, or grabbing hot pans.

## Slide 6: Washing, Storage & Tool Control
Never leave knives in the sink or under water.
Wash, rinse, sanitize, then dry immediately; no air-drying blades.
Return to the magnetic strip with handles aligned, tips up and safe.
If a magnet is full, use guards and store in the designated knife drawer.

## Slide 7: Sharpness Standards & Service
A dull knife is dangerous: hone before every shift; sharpening service every two weeks.
Test sharpness with a tomato or paper slice; if it skids or tears, re-hone or pull from service.
Use the honing steel at a steady angle; avoid grinding away the edge on boards.
Task: Honing · Tool: Honing steel · Frequency/Rule: hone before every shift
Task: Sharpening service · Tool: Pro service · Frequency/Rule: sharpening service every two weeks.
Task: Storage · Tool: Magnetic strip · Frequency/Rule: Wash, dry and return to the magnetic strip
Task: Carry through kitchen · Tool: N/A · Frequency/Rule: Carry knives point down, blade facing back

## Slide 8: How To Hone (Quick Steps)
Wipe blade clean and dry.
Hold steel vertical, tip planted on a towel.
Set 15–20° angle; draw heel to tip, light pressure.
Alternate sides, 5–8 passes each.
Wipe blade; test on tomato or paper. Repeat if needed.

## Slide 9: Mandolines, Oysters & Gloves
Cut-resistant glove on the guiding hand for mandolines and oysters.
Use the mandoline guard; never freehand small ends—switch to knife.
For oysters: stabilize towel, keep the other hand gloved and behind the tip.
Store mandolines with guards on; blade covered when not in use.

## Slide 10: What To Do If...
Knife falls: do not reach—step back, warn “Knife down!”, then pick up safely.
Board slides: stop cutting; reset with a damp towel under the board.
You get a cut: stop, wash, pressure, bandage with finger cot/glove, tell Samuel.
Knife is dull or chipped: tag “DULL/CHIP,” pull from the line, log for service.